## Slide 1
Project Management
For this project we allocated roles as shown in the table to the right. We met weekly to discus our progress as well as allocate tasks to each team member for the week.
We liaised with other academics and PhD students to assist in our project, and allocate time when we could have access to the wireless sensor nodes.
Towards Debugging of Wireless Sensor Networks
Abstract
Debugging tools are vital for developers to produce reliable software, however traditional tools are less useful when developing software for new system paradigms such as wireless sensor networks. As wireless sensor networks become increasing prevalent in our lives it will become ever more important that the software they are running works reliably and to do this debugging tools will be required. This project investigates how predicates can be specified and checked on wireless sensor node and how errors can be reported to a base station.
Background
Wireless Sensor Networks (WSNs) are a collection of small computing devices equipped with a radio (for wireless communication), sensors (to get information on the environment) and a battery to power the device.
As these devices are not attached to the mains power we need to make sure that we do as little energy intensive work (eg. Receiving/Transmitting data) as possible to lengthen the lifetime and usefulness of the network.
As energy is a limiting factor, the software developed for WSNs typically trade reliability for decreased energy usage. That means that very special care must be taken to develop programs that behave well and continue to behave well under real world conditions.
Predicate Specification
One of the requirements of our project is that we wished to specify predicates to be checked, not just at compile-time, but also at run-time. The main reason is that the needs of a system will change over time.
We explored a variety of methods of specifying predicates for evaluation, with an aim to enable an expressive syntax. However, we found that existing solutions – such as eLua (Embedded Lua) [CITE] and Wren [CITE] – were not suitable due to their high resource requirements or lack of desired features.
Thus, we implemented our own predicate-based scripting language that provided the features we wanted, and the ability to run on the limited resources available. We designed a syntax that enabled us to target nodes and utilise built in functions to iterate over sets of nodes when evaluating first-order predicates.
In order to realise this, we have implemented a parser, assembler and virtual machine. The base application will compile new predicates and transmit the assembled bytecode to nodes for execution.
As an example of a predicate specified in our language, the following snippet will check no nodes within a two-hop neighbourhood have clashing slots. This is a property that should hold in systems using the TDMA (time division multiple access) MAC protocol.
Name | Role
Matthew Bradbury | Group Leader
Tim Law | Developer and Researcher
Ivan Leong | Developer and Tester
Daniel Robertson | Project Manager
Amit Shah | Technical leader
Joe Yarnall | Developer and Tester
Second Term Plan
Predicate Specification
  Improve run-time definition and evaluation
  Reduce energy usage
Visualisation Tool
  Provide more information
  Better predicate checking integration
Performance
  Investigate where the best place to evaluate a predicate is
  Perform performance testing using physical nodes
Issues Encountered
References
using Neighbours(2) as twohopn in
@(x : twohopn ~
slot(x) != slot(this))
∀x ϵ Neighbours(2) ⋅
slot(x) ≠ slot(this)
Listing 1. A predicate in our custom language and the same predicate in first order logic
HSEND
Algorithms
When developing software for WSNs, there are several algorithms that are commonly used to perform certain tasks. So, in order to test that our solution is applicable to real world code, we have developed some of these algorithms for us to specify and check predicates for.
Tree Aggregation
Clustering
As two of the key constraints in a WSN are energy consumption and bandwidth, we made it a priority to minimise the number of messages sent through the network; clustering is perhaps the most widely-used strategy for achieving this.
Using features suggested by the Low-Energy Adaptive Clustering Hierarchy (LEACH), we devised two clustering algorithms; a basic cluster for small networks (cf. the diagram below), and a hierarchical cluster (with variable depth) which can be scaled up arbitrarily.
The basic clustering algorithm simply elects all nodes within radio range of the sink as clusterheads (CHs); all other nodes send data to their closest CH which performs some application-dependent aggregation on these messages before forwarding them on to the sink. This is only useful in small networks, as networks in which the majority of nodes aren't within range of the CHs would have to forward their messages through some path of regular nodes, thus removing the efficiency of clustering.
A common task is to have every node in a network send data to the sink, whilst having some aggregation function performed on that data. To minimise the number of retransmissions the network is orangised as a tree. In this tree a node will collect child node’s data and perform some function over that data , once all children’s information is received the aggregated result will be sent to the parent of that node. Eventually the sink will receive and aggregate information from its children. Common applications for this algorithm is to calculate the average temperature over the area monitored by the sensor network.
Hierarchical clustering also begins by electing the nodes within range of the sink as CHs at level 1, but as the setup message spreads through the network nodes whose shortest path to their nearest level n clusterhead is D hops (where D is specified in advance) also elect themselves as clusterheads and create a new cluster for level n+1. For D > 1, nodes pass messages to their CH through the other nodes in their cluster, using Contiki’s low-overhead mesh messaging protocol.
Visualisation and Interface Tool
We are developing a GUI to control our project, which will run on a computer and interface with the base station. It's main features will be predicate creation and deployment, and network visualisation.
Monitoring a new predicate will simply involve writing a predicate in our custom scripting language, and submitting it using the GUI for evaluation in the network .
In order to visualise the WSN and the state of the attached predicates, we have two main views in mind. The first is simply a list of predicates, colour coded by their current status, enabling the user to see at a glance any problems that arise. The second will be a network graph, showing the spatial relationships between nodes, associated clustering hierarchies, and generally provide a more visual representation of the WSN and attached predicates.